## Slide 1: Dr. Snehlata Barde Professor & HoD. MSIT MATS University,Raipur
Raster scan display & Random scan display

## Slide 2: Raster scan display
It is a scanning technique in which the electron beam moves along the
screen. It moves from top to bottom covering the line at a time.
When the electron beam moves in each row, the beam intensity is
turned on and off to create a pattern of illuminated states.
Picture definition is stored in a memory area called a refresh buffer or frame buffer. This memory area holds a set of intensity values ​​for all screen points. The intensity values ​​are later retrieved from the refresh buffer and appear on the screen in a row (scan line).
• The image is stored in a frame buffer containing the total screen area and
where each memory location corresponds to a pixel.
• In a monochrome system, each bit is 1 or 0 for the corresponding pixel to
be on or off (bitmap). • The display processor scans the frame buffer to turn
electron beam on/off depending if the bit is 1 or 0. • For color monitors,d,

## Slide 3
the frame buffer also contains the color of each pixel (color buffer) as
well as other characteristics of the image (gray scale, …).8 bits/pixel
 0..255 (pixmap). • Depth of the buffer area is the number of
bits per pixel (bit planes), up to 24.
Examples:
television panels, printers,PC monitors (99% of raster-scan)....
16 Raster-scan Displays
Refresh rate: 24 is a minimum to avoid flicker, corresponding to 24 Hz
(1 Hz = 1 refresh per second)
Current raster-scan displays have a refresh rate of at least 60 frames
(60 Hz) per second, up to 120 (120 Hz).
• Uses large memory: 640x480  307200 bits  38 kB
• Refresh procedure:
Horizontal retrace – beam returns to left of screen
-Vertical retrace – bean returns to top left corner of screen
– Interlaced refresh:- display first even-numbered lines, then oddnumbered lines permits to see
the image in half the time useful for slow refresh rates (30 Hz shows as 60 Hz).

## Slide 4
Active raster scan
Horizontal retrace
Vartical retrace
Disply Processor
Memory
Frame buffer
Display processor
System memory
CPU
Video controller
System Bus
Monitor
I/O Devices

## Slide 5
Advantages
It looks like a very real picture.
It can emit millions of unique colors.
It can show shadow scan.
Dis advantages
Its resolution is low.
It provides a zig zag line.

## Slide 6: Random-scan Displays
• Random scan systems are also called vector, strokewriting, or calligraphic
displays.
• The electron beam directly draws the picture in any specified order.
• A pen plotter is an example of such a system. • Picture is stored in a
display list, refresh display file, vector file, or display program as a set of
line drawing commands.
• Refreshes by scanning the list 30 to 60 times per second.
• More suited for line-drawing applications such as architecture and
manufacturing.

## Slide 7
• Advantages:
-– High resolution
– Easy animation
– Requires little memory
• Disadvantages:
– Requires intelligent electron beam (processor controlled)
– Limited screen density, limited to simple, line-based images
– Limited color capability.
• Improved in the 1960’s by the Direct
View Storage Tube (DVST) from Tektronix.

## Slide 8
System Memory
Display Processor
Monitor
System Bus
CPU
I/O Devices

## Slide 9: Difference between Raster & Random scan display
Comparison points | Raster scan | Random scan
Resolution | Its resolution is very low because the picture definition is stored as intensity value. | Its resolution is high because it is stored as a group of line commands.
Cost | It is less expensive than a random scan. | It is expensive than a raster scan.
Refresh Rate | Refresh rate is 60 to 80 frames per second. | Refresh rate is 30 to 60 times per second
Picture definition | It stores the picture definition in the refresh buffer. | It stores the picture definition in the refresh display file.
Line drawing | This provides a zig-zag line as the plotted value is different. | This provides a smooth line as the line path is followed by the electron beam.
Image drawing | Pixels are used to draw images in it. | It is used to draw applications and mathematical functions.